## Slide 1: Devil physics The baddest class on campus IB Physics

## Slide 2: Lsn 19-3: Kirchoff’s Rules

## Slide 3: Reading Activity Questions?

## Slide 4: Big Idea(s):
Changes that occur as a result of interactions are constrained by conservation laws.

## Slide 5: Enduring Understanding(s):
The energy of a system is conserved.
The electric charge of a system is conserved.

## Slide 6: Essential Knowledge(s):
Kirchhoff’s loop rule describes conservation of energy in electrical circuits. The application of Kirchhoff’s laws to circuits is introduced in Physics 1 and further developed in Physics 2 in the context of more complex circuits, including those with capacitors.
  Energy changes in simple electrical circuits are conveniently represented in terms of energy change per charge moving through a battery and a resistor.
  Since electric potential difference times charge is energy, and energy is conserved, the sum of the potential differences about any closed loop must add to zero.
  The electric potential difference across a resistor is given by the product of the current and the resistance.
  The rate at which energy is transferred from a resistor is equal to the product of the electric potential difference across the resistor and the current through the resistor.

## Slide 7: Essential Knowledge(s):
Kirchhoff’s junction rule describes the conservation of electric charge in electrical circuits. Since charge is conserved, current must be conserved at each junction in the circuit. Examples should include circuits that combine resistors in series and parallel. [Physics 1: covers circuits with resistors in series, with at most one parallel branch, one battery only.]

## Slide 8: Learning Objective(s):
The student is able to construct or interpret a graph of the energy changes within an electrical circuit with only a single battery and resistors in series and/or in, at most, one parallel branch as an application of the conservation of energy (Kirchhoff’s loop rule).
The student is able to apply conservation of energy concepts to the design of an experiment that will demonstrate the validity of Kirchhoff’s loop rule (ΣΔV = 0) in a circuit with only a battery and resistors either in series or in, at most, one pair of parallel branches.

## Slide 9: Learning Objective(s):
The student is able to apply conservation of energy (Kirchhoff’s loop rule) in calculations involving the total electric potential difference for complete circuit loops with only a single battery and resistors in series and/or in, at most, one parallel branch.
The student is able to apply conservation of electric charge (Kirchhoff’s junction rule) to the comparison of electric current in various segments of an electrical circuit with a single battery and resistors in series and in, at most, one parallel branch and predict how those values would change if configurations of the circuit are changed.

## Slide 10: Learning Objective(s):
The student is able to design an investigation of an electrical circuit with one or more resistors in which evidence of conservation of electric charge can be collected and analyzed.
The student is able to use a description or schematic diagram of an electrical circuit to calculate unknown values of current in various segments or branches of the circuit.

## Slide 11: Series Circuits
Circuits are said to be “in series” when the same current runs through them as if they were connected end to end
  The potential drop across each resistor is, V1 = IR1 , V2 = IR2 , V3 = IR3

## Slide 12: Series Circuits
For resistors in series, it is the same as replacing all resistors with one that has the total value of all in series.
For resistors in series, the same current flows through all resistors and the potential drop across the resistors is equal to the drop across the series.

## Slide 13: Series Circuits
EXAMPLE: If resistors of 2𝛀, 3 𝛀, and 7 𝛀 are connected in series in a circuit with a current of 2.5 amps what will be the emf in a source with negligible resistance?

## Slide 14: Series Circuits
EXAMPLE: If resistors of 2𝛀, 3 𝛀, and 7 𝛀 are connected in series in a circuit with a current of 2.5 amps what will be the emf in a source with negligible resistance?

## Slide 15: Parallel Circuits
In parallel circuits, the current splits and flows through two or more resistors
The current that enters the split must equal the current that exits the split
The sum of the split currents must equal the current in and out
The same potential exists across each resistor that is connected in parallel
  That is what determines the current

## Slide 16: Parallel Circuits
Consider the circuit below

## Slide 17: Parallel Circuits

## Slide 18: Series Circuits
Parallel Circuits

## Slide 19: Analyzing Circuits
The reason we have learned how to combine resistors that are in series or in parallel is that it gives us a means for analyzing circuits

## Slide 20: Analyzing Circuits
EXAMPLE: Find the current through each resistor and the potential difference across each resistor in the circuit below:

## Slide 21
In series resistors, the current through each resistor is the same and the potential difference (drop) is different.
In parallel resistors, the potential difference (drop) is the same and the current through each resistor is different.

## Slide 22: Kirchhoff’s Second Law
AKA Voltage Law, AKA Loop Law
The sum of the voltages around a circuit equal zero
  Voltage across power sources are positive
  Voltage drops across resisters are negative

## Slide 23: Kirchhoff’s Second Law
AKA Voltage Law, AKA Loop Law
The sum of the voltages around a circuit equal zero
3Ω
8 V
2Ω
1Ω

## Slide 24: Kirchhoff’s Second Law
This example illustrates the fact that series resistors can be added.
3Ω
8 V
2Ω
1Ω

## Slide 25: Kirchhoff’s First Law
AKA Current Law, AKA Junction Law
The sum of the currents going into a junction will equal the sum of the currents flowing out of a junction.
18 V
Top Loop
I1
3Ω
2Ω
1Ω
I2
I3
1Ω
21 V
Bottom Loop

## Slide 26: Kirchhoff’s Laws In Action
18 V
Top Loop
I1
3Ω
2Ω
1Ω
I2
I3
1Ω
21 V
Bottom Loop
What’s your strategy?

## Slide 27: Kirchhoff’s Laws In Action
18 V
Top Loop
I1
3Ω
2Ω
1Ω
I2
I3
1Ω
21 V
Bottom Loop

## Slide 28: Kirchhoff’s Laws In Action
18 V
Top Loop
I1
3Ω
2Ω
1Ω
I2
I3
1Ω
21 V
Bottom Loop

## Slide 29: Kirchhoff’s Laws In Action
18 V
Top Loop
I1
3Ω
2Ω
1Ω
I2
I3
1Ω
21 V
Bottom Loop

## Slide 30: Kirchhoff’s Laws In Action
18 V
Top Loop
I1
3Ω
2Ω
1Ω
I2
I3
1Ω
21 V
Bottom Loop

## Slide 31: Kirchhoff’s Laws In Action
18 V
Top Loop
I1
3Ω
2Ω
1Ω
I2
I3
1Ω
21 V
Bottom Loop

## Slide 32: Kirchhoff’s Laws In Action
18 V
Top Loop
I1
3Ω
2Ω
1Ω
I2
I3
1Ω
21 V
Bottom Loop

## Slide 33: Kirchhoff’s Laws In Action
18 V
Top Loop
I1
3Ω
2Ω
1Ω
I2
I3
1Ω
21 V
Bottom Loop
Does it check?

## Slide 34: Kirchhoff’s Laws In Action
18 V
Top Loop
I1
3Ω
2Ω
1Ω
I2
I3
1Ω
21 V
Bottom Loop
Bazinga

## Slide 35: Learning Objective(s):
The student is able to construct or interpret a graph of the energy changes within an electrical circuit with only a single battery and resistors in series and/or in, at most, one parallel branch as an application of the conservation of energy (Kirchhoff’s loop rule).
The student is able to apply conservation of energy concepts to the design of an experiment that will demonstrate the validity of Kirchhoff’s loop rule (ΣΔV = 0) in a circuit with only a battery and resistors either in series or in, at most, one pair of parallel branches.

## Slide 36: Problem Solving Strategy
Label the currents and use direction arrows going into a junction. If you guess wrong on the direction, it will just come out negative indicating the opposite direction.
Identify and label the unknowns – this determines how many equations you need.
Apply Kirchhoff’s junction rule for one or more junctions.
Apply Kirchhoff’s loop rule for one or more loops.
Solve algebraically for the unknowns.

## Slide 37: Learning Objective(s):
The student is able to apply conservation of energy (Kirchhoff’s loop rule) in calculations involving the total electric potential difference for complete circuit loops with only a single battery and resistors in series and/or in, at most, one parallel branch.
The student is able to apply conservation of electric charge (Kirchhoff’s junction rule) to the comparison of electric current in various segments of an electrical circuit with a single battery and resistors in series and in, at most, one parallel branch and predict how those values would change if configurations of the circuit are changed.

## Slide 38: Learning Objective(s):
The student is able to design an investigation of an electrical circuit with one or more resistors in which evidence of conservation of electric charge can be collected and analyzed.
The student is able to use a description or schematic diagram of an electrical circuit to calculate unknown values of current in various segments or branches of the circuit.

## Slide 39: Essential Knowledge(s):
Kirchhoff’s loop rule describes conservation of energy in electrical circuits. The application of Kirchhoff’s laws to circuits is introduced in Physics 1 and further developed in Physics 2 in the context of more complex circuits, including those with capacitors.
  Energy changes in simple electrical circuits are conveniently represented in terms of energy change per charge moving through a battery and a resistor.
  Since electric potential difference times charge is energy, and energy is conserved, the sum of the potential differences about any closed loop must add to zero.
  The electric potential difference across a resistor is given by the product of the current and the resistance.
  The rate at which energy is transferred from a resistor is equal to the product of the electric potential difference across the resistor and the current through the resistor.

## Slide 40: Essential Knowledge(s):
Kirchhoff’s junction rule describes the conservation of electric charge in electrical circuits. Since charge is conserved, current must be conserved at each junction in the circuit. Examples should include circuits that combine resistors in series and parallel. [Physics 1: covers circuits with resistors in series, with at most one parallel branch, one battery only.]

## Slide 41: Enduring Understanding(s):
The energy of a system is conserved.
The electric charge of a system is conserved.

## Slide 42: Big Idea(s):
Changes that occur as a result of interactions are constrained by conservation laws.

## Slide 43: Questions?

## Slide 44: Homework
#23-31

## Slide 45: Stopped here 4/21/15