## Slide 1: Devil physics The baddest class on campus IB Physics

## Slide 2: Lsn 5-3: electric cells

## Slide 3: Review Video: Electric Potential Voltage

## Slide 4: In the last lesson we learned:
The definition of electric current,
The definition of electric resistance,
That metallic conductors at constant temperature satisfy Ohm’s Law,

## Slide 5: In the last lesson we learned:
That the potential drops as one moves across a resistor in the direction of the current
That a resistor dissipates power,

## Slide 6: Essential idea:
Electric cells allow us to store energy in a chemical form.

## Slide 7: International-mindedness:
Battery storage is important to society for use in areas such as portable devices, transportation options and back-up power supplies for medical facilities

## Slide 8: Theory of knowledge:
Battery storage is seen as useful to society despite the potential environmental issues surrounding their disposal.
Should scientists be held morally responsible for the long-term consequences of their inventions and discoveries?

## Slide 9: Understandings:
Cells
Internal resistance
Secondary cells
Terminal potential difference
Electromotive force (emf)

## Slide 10: Applications and skills:
Investigating practical electric cells (both primary and secondary)
Describing the discharge characteristic of a simple cell (variation of terminal potential difference with time)

## Slide 11: Applications and skills:
Identifying the direction of current flow required to recharge a cell
Determining internal resistance experimentally
Solving problems involving emf, internal resistance and other electrical quantities

## Slide 12: Guidance:
Students should recognize that the terminal potential difference of a typical practical electric cell loses its initial value quickly, has a stable and constant value for most of its lifetime, followed by a rapid decrease to zero as the cell discharges completely.

## Slide 13: Data booklet reference:

## Slide 14: Aims:
Aim 6: experiments could include (but are not limited to): investigation of simple electrolytic cells using various materials for the cathode, anode and electrolyte; software-based investigations of electrical cell design; comparison of the life expectancy of various batteries

## Slide 15: Aims:
Aim 8: although cell technology can supply electricity without direct contribution from national grid systems (and the inherent carbon output issues), safe disposal of batteries and the chemicals they use can introduce land and water pollution problems

## Slide 16: Aims:
Aim 10: improvements in cell technology has been through collaboration with chemists

## Slide 17: Utilization:
The chemistry of electric cells (see Chemistry sub-topics 9.2 and C.6)

## Slide 18: Introductory Video: Why Charges Move

## Slide 19: Emf (ε)
Charges will not move in a conductor unless there exists an electric potential created by an electromotive force (emf) providing the energy
  Resistance
  Superconductors are an exception
    Since the electrons must be ‘pushed’ from the positive terminal to the negative terminal, work must be done on the electrons

## Slide 20: Emf (ε)
Emf sources
  battery - converts stored chemical energy into electrical energy
  generator – converts mechanical energy into electrical energy
  thermocouple – converts thermal energy into electrical energy
  photoelectric material – converts solar energy into electrical energy

## Slide 21: Batteries: Practical Source of Electric Current

## Slide 22: Emf (ε)
Electromotive force (emf, 𝛆) is equal to the total work done in moving a unit charge completely around a circuit
Unit for emf is the volt (V, J/C)

## Slide 23: Emf (ε)
Emf can also be defined as the total power generated by the voltage source per unit current

## Slide 24: Emf (ε)
Chemicals inside the battery create a small amount of resistance (r) which is the internal resistance of the battery
The total emf is reduced by the internal resistance of the battery, thus the potential of the battery is
Thus, the potential of a battery is always less than the emf of the battery

## Slide 25: Secondary Cells

## Slide 26: Secondary Cells
Primary cells are those that can only be used once
Secondary cells can be recharged
In circuit analysis, the potential of a recharging cell is subtracted from the emf

## Slide 27: Secondary Cells
Is this circuit drawn correctly?
2.0 Ω
4.0 Ω
2.0 Ω
6.0 Ω
12.0 V
2.0 V

## Slide 28: Secondary Cells
Is this circuit drawn correctly?
  While it appears the currents from the two cells are flowing in opposite directions, the reality is that one cell is being used to recharge the other.
2.0 Ω
4.0 Ω
2.0 Ω
6.0 Ω
12.0 V
2.0 V

## Slide 29: Secondary Cells
Which cell is being charged?
2.0 Ω
4.0 Ω
2.0 Ω
6.0 Ω
12.0 V
2.0 V

## Slide 30: Secondary Cells
Which cell is being charged?
  The 2-V cell
What will be the direction of the current?
2.0 Ω
4.0 Ω
2.0 Ω
6.0 Ω
12.0 V
2.0 V

## Slide 31: Secondary Cells
Which cell is being charged?
  The 2-V cell
What will be the direction of the current?
  Counter-clockwise
What is the current in this circuit?
2.0 Ω
4.0 Ω
2.0 Ω
6.0 Ω
12.0 V
2.0 V

## Slide 32: Secondary Cells
Which cell is being charged?
  The 2-V cell
What will be the direction of the current?
  Counter-clockwise
What is the current in this circuit?
2.0 Ω
4.0 Ω
2.0 Ω
6.0 Ω
12.0 V
2.0 V

## Slide 33: Secondary Cells
How much power is being used to charge the 2.0 V cell?
2.0 Ω
4.0 Ω
2.0 Ω
6.0 Ω
12.0 V
2.0 V

## Slide 34: Secondary Cells
How much power is being used to charge the 2.0 V cell?
2.0 Ω
4.0 Ω
2.0 Ω
6.0 Ω
12.0 V
2.0 V

## Slide 35: Battery Discharge Rates
Highly dependent on amount of current
General trend in terminal voltage:
  Initial drop
  Generally constant
  Quick drop-off

## Slide 36: Discharge Rate – Car Battery

## Slide 38: Discharge Rate – Secondary Cell

## Slide 39: Nature of Science / TOK
Consumers want:
  Longer battery life
  Quicker recharge rates
  Longer batter longevity
Battery hazards
  Mercury, lead-acid, and cadmium are toxic
  Lithium batteries can create intensely hot fires
  Unused lithium batteries provide a convenient source of lithium metal for use as a reducing agent in methamphetamine labs

## Slide 40: Nature of Science / TOK
How do we balance consumer desires with social and ecological responsibility?

## Slide 41: Applications and skills:
Investigating practical electric cells (both primary and secondary)
Describing the discharge characteristic of a simple cell (variation of terminal potential difference with time)

## Slide 42: Applications and skills:
Identifying the direction of current flow required to recharge a cell
Determining internal resistance experimentally
Solving problems involving emf, internal resistance and other electrical quantities

## Slide 43: Understandings:
Cells
Internal resistance
Secondary cells
Terminal potential difference
Electromotive force (emf)

## Slide 44: Essential idea:
Electric cells allow us to store energy in a chemical form.

## Slide 45: Questions?

## Slide 46: Homework
#30-36

## Slide 47: Stopped here 4/22/15